NDS, Inc.	March 2004

851 North Harvard Avenue

PO Box 339

Lindsay, California  93247

Toll Free	(800) 726-1994

Toll Free Fax	(800) 726-1998

Phone		(559) 562-9888

Fax		(559) 562-4488

Website	www.ndspro.com

E-Mail		nds@ndspro.com

Product Guide Specification

Specifier Notes: This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, including MasterFormat, SectionFormat, and PageFormat, contained in the CSI Manual of Practice. The section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code. Coordinate this section with other specification sections and the Drawings. Delete all “Specifier Notes” when editing this section.

SECTION 02630

PRE-SLOPED CHANNEL DRAIN SYSTEM

Specifier Notes: This section covers NDS “Dura Slope™” channel drains. Consult NDS for assistance in editing this section for the specific application.

PART 1	GENERAL

1.1	SECTION INCLUDES

A.	Pre-sloped channel drain system.

1.2	RELATED SECTIONS

Specifier Notes: Edit the following list of related sections as required for the project. Provide section numbers. List other sections with work directly related to this section.

A.	Section 02_______ - Excavation and Backfill.

B.	Section 02_______ - Drain Pipe.

1.3	SUBMITTALS

A.	Comply with Section 01330 - Submittal Procedures.

B.	Product Data:  Submit manufacturer's product data, including installation instructions.

C.	Shop Drawings:  Submit manufacturer's shop drawings, indicating layout, materials, components, accessories, and dimensions.

D.	Warranty:  Submit manufacturer's standard warranty.

1.4	QUALITY ASSURANCE

A.	Single Source Responsibility:  Provide pre-sloped channel drain system from single manufacturer.

1.5	DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage:  Store materials in clean, cool, dry area in accordance with manufacturer's instructions. Do not store materials in direct sunlight.

C.	Handling:  Protect materials during handling and installation to prevent damage.

PART 2	PRODUCTS

2.1	MANUFACTURER

A.	NDS, Inc., 851 North Harvard Avenue, PO Box 339, Lindsay, California 93247.  Toll Free (800) 726-1994.  Toll Free Fax (800) 726-1998.  Phone (559) 562-9888.  Fax (559) 562-4488.  Website www.ndspro.com.  E-Mail nds@ndspro.com.

2.2	PRE-SLOPED CHANNEL DRAINS

A.	Dura Slope Channel Drain:

1.	Description:  6-5/8-inch wide trench drain system.

a.	Material:  Molded, gray, structural-foam polyethylene with UV inhibitor.

b.	Built-In Slope:  0.7 percent.

c.	Inside Diameter:  4 inches.

d.	Bottom Radius:  2 inches.

e.	Each Modular Channel Section:  4-feet long.  Molded bottom outlet.

f.	Pre-Installed Pro Fit Locking System:  Locks grate to integral frame.

g.	Leve Loc Integral Rebar Supports:  Located at 24-inch intervals along each side of channel contain internal protruding knob to grip No.4 rebar to provide channel height adjustment during installation.

h.	Dura Loc Tongue-and-Groove Ends:  Connect to allow for precise fit and straight channel runs.

Specifier Notes: Specify Dura Slope™ channel drain system components required for the specific application. Delete components not required.

B.	7.38-Inch Deep Neutral Dura Slope Channel:

1.	Part Number:  DS-100N.

C.	7.38-Inch to 7.72-Inch Deep Dura Slope Channel:

1.	Part Number:  DS-101.

D.	7.72-Inch to 8.06-Inch Deep Dura Slope Channel:

1.	Part Number:  DS-102.

E.	8.06-Inch to 8.4-Inch Deep Dura Slope Channel:

1.	Part Number:  DS-103.

F.	8.4-Inch Deep Neutral Dura Slope Channel:

1.	Part Number:  DS-103N.

G.	8.40-Inch to 8.74-Inch Deep Dura Slope Channel:

1.	Part Number:  DS-104.

H.	8.74-Inch to 9.08-Inch Deep Dura Slope Channel:

1.	Part Number:  DS-105.

I.	9.08-Inch to 9.42-Inch Deep Dura Slope Channel:

1.	Part Number:  DS-106.

J.	9.42-Inch Deep Neutral Dura Slope Channel:

1.	Part Number:  DS-106N.

K.	9.42-Inch to 9.76-Inch Deep Dura Slope Channel:

1.	Part Number:  DS-107.

L.	9.76-Inch to 10.10-Inch Deep Dura Slope Channel:

1.	Part Number:  DS-108.

M.	10.1-Inch to 10.44-Inch Deep Dura Slope Channel:

1.	Part Number:  DS-109.

N.	10.44-Inch Deep Neutral Dura Slope Channel:

1.	Part Number:  DS-109N.

O.	10.44-Inch to 10.78-Inch Deep Dura Slope Channel:

1.	Part Number:  DS-110.

P.	10.78-Inch to 11.12-Inch Deep Dura Slope Channel:

1.	Part Number:  DS-111.

Q.	11.12-Inch to 11.46-Inch Deep Dura Slope Channel:

1.	Part Number:  DS-112.

2.3	CHANNEL GRATES

Specifier Notes: Specify Dura Slope™ channel drain grates required for the specific application. Delete grates not required.

A.	Dura Slope 2-Foot Channel Grate:

Specifier Notes: Specify Part No. 660 for White. Specify Part No. 661LG for Gray. Specify Part No. 662 for Green. Specify Part No. 663 for Black. Specify Part No. 664 for Sand. Specify Part No. 665 for Brick Red.

1.	Part Number:  [660]  [661LG]  [662]  [663]  [664]  [665].

2.	Description:  2-foot, structural-foam polyolefin, secured channel grate with UV inhibitor.

3.	Grate Openings:  1/2 inch by 3-13/16 inches.

4.	Open Surface Area:  20.61 square inches per foot.

5.	Inlet Capacity:  27.00 gpm per foot.

6.	Load:  61 to 175 psi at speeds less than 20 mph.

Specifier Notes: Specify required color. Delete colors not required.

7.	Color:  [White]  [Gray]  [Green]  [Black]  [Sand]  [Brick Red].

B.	Dura Slope 2-Foot Cast Iron Channel Grate:

1.	Part Number:  DS-231.

2.	Description:  2-foot, heavy-duty, cast iron, channel grate.

3.	Grate Openings:  5/16 inch by 4-11/16 inches.

4.	Open Surface Area:  15.27 square inches per foot.

5.	Inlet Capacity:  20.00 gpm per foot.

6.	Load:  326 to 575 psi.  H-20 rated at speeds less than 20 mph.

7.	Color:  Black.

C.	Dura Slope 2-Foot Ductile Iron Channel Grate:

1.	Part Number:  DS-232.

2.	Description:  2-foot, heavy-duty, ductile iron, channel grate.

3.	Grate Openings:  5/16 inch by 4-11/16 inches.

4.	Open Surface Area:  15.27 square inches per foot.

5.	Inlet Capacity:  20.00 gpm per foot.

6.	Load:  326 to 575 psi.  H-20 rated at speeds less than 20 mph.

7.	Color:  Black.

D.	Dura Slope 2-Foot Galvanized Steel Channel Grate:

1.	Part Number:  DS-221.

2.	Description:  2-foot, galvanized rolled steel, channel grate.

3.	Grate Openings:  3/4 inch by 4-7/16 inches.

4.	Open Surface Area:  19.85 square inches per foot.

5.	Inlet Capacity:  26.00 gpm per foot.

6.	Load:  176 to 325 psi.  H-20 rated at speeds less than 20 mph.

7.	Color:  Galvanized steel.

2.4	IN-LINE CATCH BASINS

A.	Dura Slope In-Line Catch Basin:

1.	Part Number:  DS-140.

2.	Description:  6-5/8-inch wide catch basin.

a.	Material:  Structural-foam polyethylene with UV inhibitor.

b.	Module Size:  2-feet long by 2-feet deep.

c.	Pre-Installed Pro Fit Locking System:  Locking devices for grating.

d.	Leve Loc Integral Rebar Supports:  Located along each side of catch basin contain internal protruding knob to grip No.4 rebar to provide height adjustment during installation.

e.	Dura Loc Tongue-and-Groove Ends:  Connect to allow for precise fit and straight channel runs.

f.	Outlets:  Each side of catch basin.

3.	Color:  Gray.

2.5	ACCESSORIES

A.	Pro Fit Grate Lock:

1.	Part Number:  DS-122.

B.	Universal End Cap Screws:

1.	Part Number:  DS-123.

C.	Universal End Cap:

1.	Part Number:  DS-124.

D.	Universal End Outlet:

1.	Part Number:  DS-127.

E.	Bottom Outlet Adapter:

1.	Part Number:  DS-126.

F.	Grate Screws:

1.	Part Number:  629.

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive pre-sloped channel drain system.  Notify Architect if areas are not acceptable.  Do not begin installation until unacceptable conditions have been corrected.

3.2	INSTALLATION

A.	Install pre-sloped channel drain system in accordance with manufacturer's instructions at locations indicated on the Drawings.

B.	Excavate trench to ensure proper bedding of concrete beneath and on both sides of channel.

C.	Install top of drain system level and to proper elevation.

D.	Ensure directional flow arrows located on bottom of channel are pointing in direction of flow, toward catch basin and/or evacuation outlet.

E.	Ensure catch basin is at required elevation and location to drain system.

F.	Apply silicon sealant to seal joints of drain system.

G.	Install and tape grates before placing concrete.

H.	Concrete:

1.	Place concrete beneath and on both sides of drain system.

2.	Ensure concrete has a minimum compressive strength of 3,500 psi at 28 days.

3.	Concrete shall be as specified in Section 03300.

I.	Recess top of drain system to be 1/8 inch below concrete finish grade.

3.3	PROTECTION

A.	Protect installed pre-sloped channel drain system from damage during construction.

END OF SECTION